## Slide 1: Mixed Integer Linear programming (MILP) using GAMS and Pyomo

## Slide 2: Agenda
Review mixed integer linear programming
Example 1 (Dorian auto manufacturing problem)
  Coding in GAMS
  Coding in Python
Example 2 (Power scheduling problem)
  Coding in GAMS
  Coding in Python
Example 3 (Flowshop scheduling problem)
  Coding in GAMS
  Coding in Python

## Slide 3: Review mixed integer linear programming
Mixed integer linear programming (MILP)
  f, h, and g are all linear
  x has at least one integer variable
subject to

## Slide 4: Example 1* - Dorian auto manufacturing
Dorian Auto is considering manufacturing three types of autos: compact, midsize, and large. Currently, 6,000 tons of steel and 60,000 hours of labor are available. For production of a type of car to be economically feasible, at least 1,000 cars of that type must be produced. Formulate an MILP to maximize Dorian’s profit.
Car type | Car type |  | 
 | Steel required (tons per car) | Labor required (hrs per car) | Profit yielded ($)
Compact | 1.5 | 30 | 2000
Midsize | 3 | 25 | 3000
Large | 5 | 40 | 4000

## Slide 5: Organizing information – sets
Set of all cars that can be manufactured

## Slide 6: Organizing information – parameters (1)
Let αa,* be the data table containing the steel and labor requirements
  Let αa, ‘steel’ be the steel requirement for each type of car
  Let αa, ‘labor’ be the labor requirement for each type of car
Let φa be the profit contribution of each type of car a (in $)
Car type | Car type |  | 
 | Steel required (tons per car) | Labor required (hrs per car) | Profit yielded ($)
Compact | 1.5 | 30 | 2000
Midsize | 3 | 25 | 3000
Large | 5 | 40 | 4000

## Slide 7: Organizing information – parameters (2)
Let μa be the minimum number of cars to be manufactured, if at all
Let σ be the total amount of steel available (in tons)
Let λ be the total amount of labor available (in hours)

## Slide 8: Organizing information – variables
Number of cars of each type manufactured
Binary variable – are cars of type a manufactured or not?

## Slide 9: Organizing information – objective function
Maximize: total profit from manufacturing cars
Objective function:

## Slide 10: Organizing information – constraints (1)
If cars of type a are produced, at least 1000 of them must be manufactured
These are ‘either-or’ constraints

## Slide 11: Formulating either-or constraints
Consider two constraints represented by and
Either or must be active constraints
Introduce a binary variable p to formulate an equivalent set of constraints
  Here, M is called the ‘big-M’ parameter
  M must be chosen to be a large enough value such that neither
  nor exceed it

## Slide 12: Organizing information – constraints (2)
Converting the equality constraints into inequality
If cars of type a are produced, at least 1000 of them must be manufactured

## Slide 13: Organizing information – constraints (3)
Calculating
Generalizing the constraint
(eq1)
(eq2)
type | If all steel used on a single type | If all hours spent on a single type | M
Compact |  |  | 2000
Midsize |  |  | 2000
Large |  |  | 1200

## Slide 14: Organizing information – constraints (4)
Total steel requirement should not exceed available amount
  (eq3)
Total labor requirement should not exceed available amount
  (eq4)

## Slide 15: Assembling optimization model
(eq1)
(eq2)
(eq3)
(eq4)

## Slide 16: Example 2* - Power generation scheduling (1)
A number of power stations are committed to meeting the defined electricity load demands over a day. There are 3 types of generating units available, 12 of type 1, 10 of type 2, and 5 of type 3. In addition to meeting the estimated load demands, there must be sufficient generators working at any time to make it possible to meet an increase in load of up to 15%. This increase would have to be accomplished by adjusting the output generators already operating within their permitted limits.
Which generators should be working in which periods of the day to minimized total cost?

## Slide 17: Example 2 - Power generation scheduling (2)
Time period | Demand (MW)
12 am – 6 am | 15,000
6 am – 9 am | 30,000
9 am – 3 pm | 25,000
3 pm – 6 pm | 40,000
6 pm – 12 am | 27,000
Generator | Generation data |  |  |  |  | 
 | Minimum level (MW) | Maximum level (MW) | Cost per hour at minimum (£/hr) | Cost per hour per MW above minimum (£/hr/MW) | Cost (£) | Number of availabilities
G1 | 850 | 2000 | 1000 | 2.0 | 2000 | 12
G2 | 1250 | 1750 | 2600 | 1.3 | 1000 | 10
G3 | 1500 | 4000 | 3000 | 3.0 | 500 | 5

## Slide 18: Organizing information – sets
Set of time periods in a day
Set of generators

## Slide 19: Organizing information – parameters (1)
δt is the demand during each time period t (in MW)
Time period | δt (MW)
12 am – 6 am | 15,000
6 am – 9 am | 30,000
9 am – 3 pm | 25,000
3 pm – 6 pm | 40,000
6 pm – 12 am | 27,000

## Slide 20: Organizing information – parameters (2)
αg, * is the generation data
  αg, min_pow is the minimum power generated by type g (in MW)
  αg, max_pow is the maximum power generated by type g (in MW)
  αg, min_cost is the cost per hour at minimum power (in £/hr)
  αg, inc_cost is the cost incurred per MW above the minimum (in £/hr/MW)
  αg, start is the cost associated with the startup of each generator g (in £)
  αg, gen_lim is the number of units of type g available
Generator | α(g,*) |  |  |  |  | 
 | min_pow | max_pow | min_cost | inc_cost | start | gen_lim
G1 | 850 | 2000 | 1000 | 2.0 | 2000 | 12
G2 | 1250 | 1750 | 2600 | 1.3 | 1000 | 10
G3 | 1500 | 4000 | 3000 | 3.0 | 500 | 5

## Slide 21: Organizing information – parameters (3)
θt is the number of hours in each time period t (in hours):
εg,t is the cost per hour for operation of generator g at minimum level multiplied by the number of hours in the period t (in £):
φg,t is the cost incurred per hour per megawatt for operation of generator g at multiplied by the number of hours in the period t (in £/MW):
Time period | θt (hr)
12 am – 6 am | 6
6 am – 9 am | 3
9 am – 3 pm | 6
3 pm – 6 pm | 3
6 pm – 12 am | 6

## Slide 22: Organizing information – variables
Output of generator g during time period t (in 1000s of MW) – non-negative-continuous variable
Number of generators of type g in use during time period t – non-negative-integer variable
Number of generators of type g started up during time period t – non-negative-integer variable

## Slide 23: Organizing information – objective function
Minimize: total cost from meeting power demand
  Total cost = Total cost of running generators at minimum power +
  Total start up cost +
  Total cost of running generators above minimum power
Objective function:

## Slide 24: Organizing information – constraints (1)
Power demand satisfaction
Spinning reserve requirement
Start-up definition
(eq1)
(eq2)
(eq3)

## Slide 25: Organizing information – constraints (2)
Minimum generation levels
Maximum generation levels
Maximum number of generators
(eq4)
(eq5)
(eq6)

## Slide 26: Assembling optimization model
(eq1)
(eq5)
(eq3)
(eq4)
(eq2)
(eq6)

## Slide 27: Example 3* - Flow shop scheduling
A workshop that produces metal pipes on demand for the automobile industry has three machines for bending the pipes, soldering the fastenings and assembling the links. The workshop has to produce 6 pieces. Every workpiece first goes to bending, then to soldering, and finally to the assembly of the links. Once started, any operations must be carried out without interruption, but the workpieces may wait between the machines. Every machine only processes one piece at a time. A workpiece may not overtake any other by passing onto the following machine. This means that if, at the beginning, a sequence of the workpieces is established, they will be processed on every machine in exactly this order. Which is the sequence of workpieces that minimizes the total time for completing all pieces?

## Slide 28: Organizing information – sets
Set of all workpieces to be worked upon
Set of all machines
(Alias) set of items

## Slide 29: Organizing information – parameters
τm,i is the processing time (in hours) associated with each machine m for each workpiece i
Machines | Workpieces |  |  |  |  | 
 | i1 | i2 | i3 | i4 | i5 | i6
bending | 3 | 6 | 3 | 5 | 5 | 7
soldering | 5 | 4 | 2 | 4 | 4 | 5
assembly | 5 | 2 | 4 | 6 | 3 | 6

## Slide 30: Organizing information – variables
Rank of item i is position k
Start time for job in position k on machine m
Completion time for job in position k on machine m
Completion time of the final ranked job on the last machine

## Slide 31: Organizing information – objective function
Minimize: total processing time, or the completion time of final ranked job on last machine
Objective function:

## Slide 32: Organizing information – constraints (1)
Every position gets a job
Every job is assigned a rank
Relations between the end of job ranked k, and start of job ranked k + 1 on machine m
(eq1)
(eq2)
(eq3)

## Slide 33: Organizing information – constraints (2)
Relations between the end of job ranked k on machine m, and start of job ranked k on machine m+1
Calculation of completion time based on start time and processing time
Completion time of job ranked last
(eq4)
(eq5)
(eq6)

## Slide 34: Assembling optimization model
(eq1)
(eq6)
(eq3)
(eq4)
(eq5)
(eq2)

## Slide 35: Example 3 – results (GAMS)
Solver: CPLEX
T = 35 minutes

## Slide 36: Example 3 – results (GAMS)
Solver: CBC
T = 35 minutes

## Slide 37: Example 3 – results (Pyomo)
Solver: CPLEX
T = 35 minutes

## Slide 38: Example 3 – results (Pyomo)
Solver: CBC
T = 35 minutes

## Slide 39: Summary
In this section, we learnt
  The general structure of a mixed integer linear optimization problem
  Introduction to coding simple MILP models in GAMS and Pyomo
  Defining “either-or” constraints using big-M
  Exporting data from Pyomo and GAMS
  Accessing elements dynamically in GAMS and Pyomo
  Submitting jobs on NEOS (for GAMS and Pyomo platforms)
  Visualizing results for scheduling problems